## Slide 1: Review Draft KRGSA Groundwater Sustainability Plan (GSP)
Kern River Groundwater
Sustainability Agency (KRGSA)
Special
Board Meeting
August 21, 2019

## Slide 2: KRGSA Sustainability Goal
Manage groundwater resources sustainably in the KRGSA Plan Area to:
    support current and future beneficial uses of groundwater including municipal, agricultural, industrial, domestic, public supply, and environmental uses
    optimize conjunctive use of surface water and groundwater
    avoid or eliminate undesirable results over the implementation and planning horizon.
Notes: edited

## Slide 3: KRGSA GSP Organization
1 Administrative Information
2 Plan Area
3 HCM/Groundwater Conditions
4 Water Budgets
5 Sustainable Management Criteria
6 Monitoring Networks
7 Projects and Management Actions
8 Implementation Plan
9 References and Technical Studies

## Slide 4: KRGSA GSP Plan Area
361 square miles
13% of the Kern County Subbasin
Composed of:
  City of Bakersfield
  Improvement District No. 4 (KCWA)
  Kern Delta Water District (KDWD)
  Additional smaller agencies
DRAFT

## Slide 5: Land Use in the KRGSA Plan Area
North – Urban
South – Agricultural
2015 Land Use
  41% - Agricultural
  33% - Urban
  26% - Undeveloped
DRAFT
7th Standard Rd

## Slide 6: Agricultural Lands in the KRGSA
90,000 acres irrigated agriculture in southern Plan Area
16,000 acres irrigated lands in northern Plan Area
20 Dairies in southern Plan Area
DRAFT
7th Standard Rd
2016 Data

## Slide 7: Active Wells in the KRGSA
162 Municipal wells
67 Public Supply and Small Water System wells
151 Industrial, Domestic, and other Private wells
642 Agricultural wells
54 Banking recovery wells
DRAFT
7th Standard Rd

## Slide 8: Preliminary Management Areas (MA)
Based on land use and well use
  Urban MA – 41%
  Agricultural MA – 57%
  Banking – 2%
DRAFT
Urban MA
Agricultural MA
Banking
MA

## Slide 9: Sustainability Indicators
Chronic Lowering of Water Levels
Reduction of Groundwater Storage
Degradation of Water Quality caused by management actions
Land subsidence affecting land use
Depletion of Interconnected Surface Water affecting beneficial use
If a sustainability indicator is determined to be significant and unreasonable , then it is an Undesirable Result
DRAFT

## Slide 10: Chronic Lowering of Water Levels
Undesirable results: when significant and unreasonable impacts occur over the implementation/planning horizon, as determined by depth/elevation of water, affect the reasonable and beneficial use of, and access to, groundwater by overlying users.
Impacts focus on groundwater wells
Balance the need for:
  higher water levels in municipal wells
  lower water levels in irrigation and banking wells, primarily to provide critical supplies during multi-year droughts.
DRAFT

## Slide 11: Historic Low WLs Impacts to Wells
Comparison of depth to water and top of municipal well screens
During 2015, water levels were below the top of screens in more than 40 municipal wells
Significant expenditures for lowering pumps, wells offline, securing supplemental supplies
DRAFT
7th Standard Rd

## Slide 12: Concentrated pumping in banking and ag wells
More than 150 municipal wells intermingled with more than 50 banking recovery wells
642 Agricultural wells, mostly southern Plan Area
Urban wells extend into the south-central Plan Area
DRAFT
7th Standard Rd

## Slide 13: Reduction of Groundwater in Storage
3 Independent Methods
Relatively good agreement
Minimal deficits; sustainable budget
Deficit for banking adjustments

## Slide 14: Projected Water Budgets Future Deficits
DRAFT
Increase urban demand
Decrease SWP supply
Increase agricultural demand (climate changes factors )
Potential Future Water Budget Deficits
Plus Historical Adjusted deficit of -29,000 AFY

## Slide 15: Projected Water Budgets C2VSimFG-Kern Model
DRAFT
Baseline - current land use and projected water supply and demand
2030 Climate Change Scenario with increases in agricultural demand and decreased supply
2070 Climate Change Scenario with further increase in demand and decrease in supply
0
Model simulates the physical system and includes recharge in the KRGSA for and by others (i.e, not KRGSA water). KRGSA is planning for larger deficits than indicated in the model.

## Slide 16: Constituent of Concern Arsenic
Focus on constituents affected by management actions
Arsenic concentrations increase with declining water levels
More than 25 wells with detections above the MCL
Widespread issue in the Plan Area
DRAFT
7th Standard Rd

## Slide 17: Inelastic Land Subsidence
Historical Subsidence from 1926 – 1970 mapped by USGS
Up to 9 feet in southern Plan Area
Correlates to areas of clay soils (and subsurface clay sediments) in south and east Plan Area
DRAFT
Clay Soils
Kern Lake Bed
Clay Soils
7th Standard Rd

## Slide 18: Recent Drought Subsidence
Recent subsidence May 2015 – Dec 2016 from NASA/JPL data
Minimal subsidence in northern Plan Area
-4 to -8 inches in southern Plan Area
Recent subsidence in same areas as historical subsidence
DRAFT
Northern KRGSA <1 inch to 1.5 inches
Central KRGSA -1.5 to -3 inches
Southern KRGSA -4 to -8 inches
7th Standard Rd
NASA/JPL May 2015 – Dec 2016

## Slide 19: Subsidence and Critical Infrastructure
Critical infrastructure includes pipelines, canals, utilities, structures, wells, transportation
No damage to critical infrastructure in the Plan Area identified to date
Set minimum thresholds to mitigate future subsidence
DRAFT

## Slide 20: Analysis of Interconnected Surface Water
DRAFT
Evaluated groundwater conditions using local NCCAG* maps along Kern River
Kern River is actively managed through regulated releases, diversions, and managed aquifer recharge
Kern River
*NCCAG - Natural Communities Commonly
Associated with Groundwater
More than 80% of the flow is diverted above the Calloway Weir
River was dry below the Calloway Weir more than 25 % of the time
Groundwater is deeper than 50’ below the river throughout the entire KRGSA

## Slide 21: Analysis of Interconnected Surface Water
DRAFT
Evaluated groundwater conditions at local NCCAG areas in southern Plan Area
Analysis indicates that local vegetation and wetlands are not supported by groundwater in the Principal Aquifer
*NCCAG - Natural Communities Commonly
Associated with Groundwater
Mapped areas include recharge basins, spills along the rim canal, artificially-constructed ski lakes. Local irrigation and perched water conditions throughout the area.

## Slide 22: Sustainability Considerations
WL below screens in Municipal Wells
Deficits for Projected Water Budgets
Arsenic in Municipal Wells
Ability of banking recovery wells to recover water
Historical subsidence
DRAFT

## Slide 23: Approach to Minimum Thresholds
Undesirable results relate historic low water levels; keep urban wells near historic lows.
Allow operational flexibility for banking wells to recover critical supplies during drought.
Measurable Objectives are selected as the midpoint for an operational range.
Keep MTs and MOs SIMPLE to facilitate management.

## Slide 24: Approach to Minimum Thresholds
Add number of wells and duration to refine definition of undesirable results.

## Slide 25: Assignment of MT, MO, and Operational Range

## Slide 26: Preliminary GSP Monitoring Wells
36 wells identified
Currently monitored in other WL programs:
  Kern Fan Monitoring Comm
  KCWA/ID4 WL Program
  City Monitoring Wells
  KDWD Monitoring Programs
Possible additional Urban MA wells from Cal Water and ENCSD
DRAFT

## Slide 27: KRGSA Subsidence Monitoring
Water level monitoring
Three GPS stations for screening
InSAR Subsidence available from DWR (on 1-mile grids)
Coordinate with KGA and other GSAs for regional Subbasin-wide subsidence monitoring
DRAFT
7th Standard Rd
NASA/JPL May 2015 – Dec 2016

## Slide 28: Key Management Projects
DRAFT
  Optimizes Kern River recharge across the southern Plan Area
  Reduces groundwater pumping
  Allows local maintenance of water levels
  SEIR completed 2018 – implementation initiated
KDWD Kern River Water Allocation Plan

## Slide 29: Key Management Projects
DRAFT
  Prioritizes use of City’s available Kern River water
  Increasing water availability over the implementation and planning horizon
  Allows municipal pumping to be reduced to avoid undesirable results
  Meets future projected water budget deficits for urban demand
City of Bakersfield Optimized Conjunctive Use

## Slide 30: Key Management Projects
DRAFT
Consolidation of up to six small water systems with ENCSD to address water quality concerns: nitrate, TCP, and arsenic
Grant funding through the DWRSF program
Improves drinking water quality for disadvantaged communities in the KRGSA
East Niles Community Services District
North Weedpatch Highway Consolidation
1,2,3-TCP Wellhead Treatment

## Slide 31: Management Actions
DRAFT
5-Step Action Plan if Minimum Thresholds are exceeded
Implement well metering in the Agricultural MA (KDWD)
Program for reporting groundwater extractions in the KRGSA
Conserve recycled water in the KRGSA Plan Area (City)
Support Delta Conveyance to preserve imported supplies
Incorporate Climate Change Adaptation Stratgies (ID4)
Improve monitoring program
Coordinate water quality analysis with existing programs

## Slide 32: Projected Water Budgets with Projects
DRAFT
0
Collectively, these projects and management actions address current and projected groundwater deficits to achieve sustainable management.

## Slide 33: 90-Review Period and Outreach
DRAFT
Communication and outreach with Stakeholders for GSP input
Outreach accomplished at many levels:
  Agency Board Meetings and Workshops
  Targeted community meetings
  Coordinate with other GSAs on Open House
GSP is a draft document and can be revised based on input:
  Working to improve monitoring program
  Incorporate details on how GSP implementation can be achieved
KRGSA supports collaborative efforts and internal coordination to achieve sustainable management for the Subbasin shared groundwater resources

## Slide 34: Questions?